## Slide 1: 자율주행 자동차에서의 전반적인 ROS 구성
YU-ANTL R&D Report
January 25 , 2021
Seong-Eun Yang, Yu-na Park
Advanced Networking Technology Lab. (YU-ANTL)
Dept. of Information & Comm. Eng, Junior in
Yeungnam University, KOREA
(Tel : +82-53-810-3940; Fax : +82-53-810-4742
http://antl.yu.ac.kr/; E-mail : yse09@ynu.ac.kr, yu07na06@ynu.ac.kr)

## Slide 2: Outline
ROS node map
ROS code

## Slide 3: ROS node map

## Slide 4
https://mushr.io/tutorials/overview/

## Slide 5: ROS code

## Slide 6: ROS code
Include
  rospy : ROS API에 대한 기본 python 인터페이스
  ackermann_msg : 드라이브 명령을 보내기 위한 공통 인터페이스
  geometry_msgs : 자동차의 초기 위치를 시뮬레이터로 보내기 위함
  quaternion_from_euler : 오일러 각도를 이용하여 계산하기 위함
import rospy
from ackermann_msgs.msg import AckermannDrive, AckermannDriveStamped
from geometry_msgs.msg import (
Point,
Pose,
PoseWithCovariance,
PoseWithCovarianceStamped,
Quaternion,
)
from tf.transformations import quaternion_from_euler

## Slide 7: ROS code
main
  실행 스레드가 시작되는 곳
  rospy.init_node(…) : 노드 초기화, 모든 노드는 자신을 ROS환경에 등록해야하기에 노드의 이름을 전달함.
  rospy.get_param(매개변수의 이름, 기본값) : 매개 변수 서버에서 값을 가져오는 함수
  rospy.Publisher(주제 이름, 메시지 유형, 대기열 크기) : ROS 메시지 전달 패러다임의 일부
if __name__ == "__main__":
rospy.init_node("path_publisher") #통신 스트림을 설정, 노드가 다른 사람들과 통신할 수 있도록
control_topic = rospy.garam("~control_topic", "/car/mux/ackermann_cmd_mux/input/navigation")
pub_controls = rospy.Publiset_pher(control_topic, AckermannDriveStamped, queue_size=1)
init_pose_topic = rospy.get_param("~init_pose_topic", "/initialpose")
pub_init_pose = rospy.Publisher(init_pose_topic, PoseWithCovarianceStamped, queue_size=1)
plan_file = rospy.get_param("~plan_file")
with open(plan_file) as f:
plan = f.readlines()
rospy.sleep(1.0)
run_plan(pub_init_pose, pub_controls, plan)

## Slide 8: ROS code
main loop of node
  노드의 메인 루프
  send_init_pose로 초기 위치 메시지를 생성 후, send_comman로 시뮬레이터에 자동차를 배치할 위치를 알림.
def run_plan(pub_init_pose, pub_controls, plan):
init = plan.pop(0)
send_init_pose(pub_init_pose, init)
for c in plan:
send_command(pub_controls, c)

## Slide 9: ROS code
Function(1)
  초기 위치(x, y, 정 및 변환하는 메시지 생성 함수
  방향은 ROS 패키지에서 제공하는 오일러 각도 quaternion_from_euler를 사용함.
def send_init_pose(pub_init_pose, init_pose):
pose_data = init_pose.split(",")
assert len(pose_data) == 3
x, y, theta = float(pose_data[0]), float(pose_data[1]), float(pose_data[2])
q = Quaternion(*quaternion_from_euler(0, 0, theta))
point = Point(x=x, y=y)
pose = PoseWithCovariance(pose=Pose(position=point, orientation=q))
pub_init_pose.publish(PoseWithCovarianceStamped(pose=pose))

## Slide 10: ROS code
Function(2)
rospy.Duration(1.0) : 1초에 한번 루프가 종료
rospy.Rate(10) : 1초 동안 최대 10번의 루프가 실행
루프 실행 빈도를 제한하기 위함
def send_command(pub_controls, c):
cmd = c.split(",")
assert len(cmd) == 2
v, delta = float(cmd[0]), float(cmd[1])
dur = rospy.Duration(1.0)
rate = rospy.Rate(10)
start = rospy.Time.now()
drive = AckermannDrive(steering_angle=delta, speed=v)
while rospy.Time.now() - start < dur:
pub_controls.publish(AckermannDriveStamped(drive=drive))
rate.sleep()